MISSION: VEGA-1 AND VEGA-2                                                    
                                                                              
INSTRUMENT: PLASMAG-1 electrostatic plasma analyzer                           
                                                                              
Mass: 9 kg                                                                    
Dimensions: non applicable                                                    
Date built: 1983-84                                                           
Manufacturer: Space Research Institute, Moscow, USSR                          
              Central Research Institute for Physics, Budapest, Hungary       
                                                                              
Instrument overview                                                           
                                                                              
The PLASMAG-1 instument package included six different sensors:               
A0 plasma impact detector for measuring neutral particle flux,                
   (manufactured by R. Grard, ESA/ESTEC, Noordwijk, The Netherlands)          
A1 Faraday cup for measuring integral ion flux from solar direction,          
A2 Faraday cup for measuring integral ion flux and neutral particles          
   from ram direction,                                                        
A3 spherical electrostatic analyzer for measuring ions from ram direction     
   in the energy range of 15 eV - 3.6 keV in 120 logarithmically              
   spaced channels,                                                           
A4 spherical electrostatic analyzer for measuring ions from solar direction   
   in the energy range of 60 eV - 30 keV in 60 logarithmically                
   spaced channels,                                                           
A5 cylindrical electrostatic analyzer for measuring ions perpendicular        
   to the ecliptic plane in the energy range of 2 eV - 10 keV in              
   30 logarithmically spaced channels.                                        
                                                                              
Scientific objectives                                                         
                                                                              
The electrostatic ion analyzers A3 and A4 were designed to study              
the change of the energy distribution of the solar wind and cometary          
ions as a function of the distance from the nucleus. The                      
detector oriented in the ram direction could determine the mass               
distribution of cometary ions close to the nucleus with a                     
resolution of m/dm=20-25.                                                     
The ram Faraday cup A2 had four modes of operation. Two of these              
provided information on the neutral particle flow from the comet.             
                                                                              
For further informations on instrument overview and scientific                
objectives (also first results) see the following papers:                     
1) Gringauz et al., The Vega probe instrument for measuring                   
charged particles with energies less than 25 keV, in "Cometary                
exploration Vol. III., ed. by T.I. Gombosi, pp. 333-350, Central Res.         
Inst. Physics, Budapest, 1982.                                                
2) Gringauz et al., First in situ plasma and neutral gas measurements         
at comet Halley, Nature 321, 282-285, 1986.                                   
3) Apathy et al., Plazmag-1 experiment, in Exploration of                     
Halley's comet, ESA SP-250, Vol. I., ed. by B. Battrick, E.J.                 
Rolfe, and R. Reinhard, pp. 65-70, Paris, 1986.                               
                                                                              
Operational considerations                                                    
                                                                              
The sensitivity of the electron analyzer A5 was very low.                     
Detectors A3 and A5 of Vega-1 were fatally damaged during the cruise phase.   
Detector A3 of Vega-2 was fatally damaged 2.5 min before closest approach.    
The channeltrons of A3 were saturating at higher count rates.                 
                                                                              
Calibration description                                                       
                                                                              
The sensors were calibrated at the Max-Planck-Institut for Aeronomy           
in Katlenburg/Lindau, Germany. The viewing angle and energy resolution        
of the electrostatic analyzers were determined in vacuum chamber              
using monoenergetic ion and electron beams, respectively.                     
(For further details see reference #3 above.)                                 
The spectrometers used Soviet-made channeltrons as particle detectors.        
An in-flight calibration was performed every day to select the                
optimum voltage for the channeltrons.                                         
A post-launch calibration was performed in order to correct the saturating    
count rates of detector A3 of Vega-2 using the integral fluxes provided       
by the ram Faraday cup A2.                                                    
                                                                              
Principal investigator: K.I. Gringauz, Space Res. Inst., Moscow,              
Co-principal investigator: T.I. Gombosi, Cent. Res. Inst. Physics, Budapest,  
Co-investigators: A.P. Remizov, M.I. Verigin, L.I. Denchikova, A.V. Dyachkov, 
                  I.N. Klimenko, G.A, Vladimirova, Space Res. Inst., Moscow   
                  I. Apathy, T. Szemerey, S. Szendro, A.J. Somogyi, K. Szego, 
                  M. Tatrallyay, A. Varga, Cent. Res. Inst. Physics, Budapest,
                  E. Keppler, Max-Planck-Inst. Aeronomy, Lindau, Germany.     
                                                                              
Instrument section                                                            
                                                                              
Field of view of the detectors: A1: 90x90 deg (centered on solar direction),  
                                A2: 26x26 deg (centered on ram direction),    
                                A3: 32x12 deg (centered on ram direction),    
                                A4: 36x32 deg (centered on solar direction),  
                                A5: 7x7 deg (perpendicular to ecliptic plane).
                                                                              
Effective apperture: A1: 1.6 cm**2                                            
                     A2: 0.93  cm**2                                          
                     A3: 0.0193 cm**2                                         
                     A4: 0.00455 cm**2                                        
                     A5: 0.0036  cm**2                                        
                                                                              
Energy resolution:   A3: 3.2 %                                                
                     A4: 3.85%                                                
                     A5: 7.5 %                                                
                                                                              
One complete spectrum was taken by A3, A4, and A5 in every                    
second during the BRL (high telemery rate) seance.                            
Sampling times for each energy channel:                                       
                     A3: 0.005 sec                                            
                     A4: 0.005 sec                                            
                     A5: 0.021 sec                                            
                                                                              
During the cruise phase data were recorded by an on-board                     
magnetometer at lower telemetry rate.                                         
                                                                              
DATA SET - VEGA-1                                                             
                                                                              
The data were measured during the BRL seance on March 6, 1986.                
                                                                              
1. parameter: time in sec - end of a 10 sec averaging interval                
              (0 sec is 4:00 UT in spacecraft time)                           
2-60. parameters: count rates observed by A4 (ions from solar direction)      
                                                                              
The energy levels for the 59 channels of detector A4 in eV:                   
    70.4    75.7    87.1    90.6   101.2   113.5   123.2   131.6   150.5   167
2                                                                             
   183.0   204.2   226.2   253.4   281.6   308.0   341.4   380.2   423.3   471
7                                                                             
   522.7   583.4   650.3   722.5   799.0   887.9   988.2  1103.5  1223.2  1360
5                                                                             
  1511.8  1672.9  1859.4  2074.2  2289.8  2556.4  2824.8  3147.8  3497.1  3899
3                                                                             
  4331.4  4842.6  5380.3  6000.7  6651.0  7302.2  8132.1  9081.6 10137.6 11308
0                                                                             
 12496.0 13921.6 15576.0 17344.8 19228.0 21348.8 23830.4 26435.2 29515.2      
                                                                              
Measurements were performed in every sec, data provided here                  
are 10 sec averages.                                                          
                                                                              
Time of first observation:  4:17:29 UT                                        
Time of first data in file: 4:17:38 UT (1058 sec)                             
Time of last observation:   8:25:08 UT                                        
Time of last data in file:  8:25:08 UT (15908 sec)                            
There was no longer data gap than a few seconds.                              
Missing or bad data: -999                                                     
                                                                              
Detectors A3 and A5 were fatally damaged before the encounter.                
                                                                              
DATA SET - VEGA-2                                                             
                                                                              
The data were measured during the BRL seance on March 9, 1986.                
                                                                              
1. parameter: time in sec - end of a 10 sec averaging interval                
              (0 sec is 4:00 UT in spacecraft time)                           
2-30. parameters: count rates observed by A5 (electrons)                      
31-90. parameters: count rates observed by A4 (ions from solar direction)     
91-210. parameters: count rates observed by A3 (ions from ram direction)      
                                                                              
The energy levels for the 29 channels of detector A5 in eV:                   
     1.9     2.9     3.8     5.8     7.7    10.6    14.9    19.2    25.9    35
0                                                                             
    47.0    61.0    84.5   113.3   168.2   229.7   311.3   410.9   553.0   744
8                                                                             
   999.2  1349.0  1804.8  2430.2  3225.2  4364.7  5869.9  7868.0 10571.0      
                                                                              
The energy levels for the 60 channels of detector A4 in eV:                   
    64.0    73.8    78.7    88.6    94.3   103.3   114.0   128.7   138.6   154
2                                                                             
   173.8   188.6   209.1   235.3   255.0   286.2   317.3   351.0   387.0   431
3                                                                             
   480.5   534.6   594.5   660.9   734.7   818.4   912.7  1014.3  1123.4  1246
4                                                                             
  1384.2  1531.8  1689.2  1877.8  2099.2  2341.1  2606.0  2896.2  3214.4  3575
2                                                                             
  3985.2  4436.2  4936.4  5494.0  6117.2  6724.0  6724.0  7544.0  8388.6  9290
6                                                                             
 10291.0 11439.0 12783.8 14268.0 15924.4 17728.4 19647.2 21861.2 24403.2 27191
2                                                                             
                                                                              
The energy levels for the 120 channels of detector A3 in eV:                  
    15.6    17.2    18.9    19.7    20.5    22.1    23.0    24.6    27.1    28
3                                                                             
    29.5    30.8    32.0    33.2    34.4    35.7    36.9    38.1    39.4    40
6                                                                             
    41.8    43.5    45.1    45.9    46.7    48.0    50.0    51.3    52.5    54
9                                                                             
    57.4    59.4    61.5    64.0    66.8    69.7    73.0    76.7    80.8    84
9                                                                             
    89.4    93.9    98.4   102.9   107.4   112.3   117.7   123.0   128.7   134
5                                                                             
   140.6   147.2   154.2   161.5   169.3   177.1   185.3   194.3   203.8   213
2                                                                             
   223.0   234.1   245.6   257.5   269.8   282.9   296.4   310.0   323.9   337
8                                                                             
   352.2   366.5   381.3   398.5   418.2   440.3   464.1   487.9   512.5   537
1                                                                             
   561.7   587.9   615.8   645.3   676.5   710.9   747.8   787.2   828.2   870
8                                                                             
   914.3   959.4  1005.3  1052.9  1102.1  1152.1  1203.8  1262.0  1325.1  1393
2                                                                             
  1466.2  1539.1  1612.9  1687.6  1763.0  1845.0  1935.2  2033.6  2140.2  2248
4                                                                             
  2358.3  2469.8  2583.8  2702.7  2829.8  2966.8  3112.7  3268.5  3432.5  3604
7                                                                             
                                                                              
Measurements were performed in every sec, data provided here                  
are 10 sec averages.                                                          
                                                                              
Time of first observation:  4:13:00 UT                                        
Time of first data in file: 4:13:10 UT (790 sec)                              
Time of last observation:   8:40:00 UT                                        
Time of last data in file:  8:40:00 UT (16800 sec)                            
There was a data gap between 7:17:30 UT (11850 sec) and 7:45:10               
(13510 sec).                                                                  
Missing or bad data: -99                                                      
                                                                              
The detector A3 was fatally damaged at 7:17:31 UT when the telemetry          
connection also broke down.                                                   
At 7:45:10 UT the connection with the instrument was re-established.