Astronomical  Data  Center



                             FITS  Table  Browser



                                 User's  Guide



                                 Version 2.0.1


                                Lee E. Brotzman



                                 November 1991


                             Contract NAS 5-30960


                                 Prepared for:

                 National Aeronautics and Space Administration
                          Goddard Space Flight Center
                              Greenbelt, MD 20771


                                 Prepared by:

                                  Hughes STX
                               4400 Forbes Blvd.
                            Lanham, Maryland 20706




  ___________________________________________________________________________
 |                                                                           |
 | This software was developed with Federal funds (Contract NAS5-30960) by   |
 |                                                                           |
 | the Astronomical Data Center (ADC), under the direction of the National   |
 |                                                                           |
 | Space Science Data Center of NASA Goddard Space Flight Center. Therefore, |
 |                                                                           |
 | this software is in the Public Domain. Although the software has been     |
 |                                                                           |
 | tested, no warranty, expressed or implied, is made by NASA or the ADC     |
 |                                                                           |
 | as to the accuracy and functioning of the software nor shall the fact of  |
 |                                                                           |
 | distribution constitute any such warranty, and no responsibility is       |
 |                                                                           |
 | assumed by NASA or the ADC in connection therewith.                       |
 |                                                                           |
 |                                                                           |
 | Written by: Mr. Lee E. Brotzman                                           |
 |             Astronomical Data Center - Hughes STX                         |
 |             Code 930.3                                                    |
 |             NASA Goddard Space Flight Center                              |
 |             Greenbelt, Maryland 20771                                     |
 |             (301) 286-6953 FTS: 888-6953                                  |
 |             Internet:   brotzman@ndadsa.gsfc.nasa.gov                     |
 |             DECNET:     NDADSA::BROTZMAN                                  |
 |             BITNET:     ZMLEB@SCFVM                                       |
 |___________________________________________________________________________|



    Contents

    1  Overview                                                     1
       1.1  References  ..........................................  1

    2  Installing FTB                                               3

    3  Starting up FTB                                              4
       3.1  Entering FTB commands  ...............................  4

    4  Using FTB                                                    5

    5  Future Developments                                          6

    6  FTB Command Reference                                        7
       6.1  BROWSE   .............................................  8
       6.2  CLOSE  ...............................................  8
       6.3  DISPLAY  .............................................  8
       6.4  DOS  .................................................  9
       6.5  ECHO  ................................................  9
       6.6  EXECUTE  ............................................. 10
       6.7  EXIT   ............................................... 10
       6.8  EXTRACT  ............................................. 10
       6.9  HELP  ................................................ 10
       6.10 LIST  ................................................ 11
       6.11 OPEN  ................................................ 11
       6.12 QUIT  ................................................ 11
       6.13 REMARK  .............................................. 11
       6.14 SELECT  .............................................. 12
       6.15 TABLE  ............................................... 13

    7  Receiving Updates                                           13

    8  Acknowledgments                                             13


Page 1

1    Overview

The Astronomical Data Center (ADC) FITS Table Browser (FTB) displays the
contents of standard Flexible Image Transport System (FITS) table extension
files on IBM PC/AT/XT-compatible MS-DOS computers. It was written specifically
to accompany the ADC CD-ROM Selected Astronomical Catalogs, Vol. I, No. 2, FITS
Table Version (Brotzman & Gessner 1991), but also works with FITS tables stored
on other direct access media.

FTB reads standard FITS files that adhere to the rules for tables extensions
described by the NASA Office of Standards and Technology (NOST) FITS
Implementation Draft Standard (NOST 100-0.1g, 1991), however, FTB should not be
viewed as a tool to verify that a particular FITS file conforms completely with
the standard. FTB works with standard FITS files containing mixtures of tables,
images, and standard extensions, but it may also work with files that break the
rules. It all depends on which rules are broken. On the other hand, FTB may
crash when confronted with standard FITS files that contain non-standard
extensions.

Table 1 lists the commands available to FTB users. Any command that FTB does not
recognize is passed on to DOS. So, for example, commands to change and list
directories (cd and dir) are executed as if they were issued from an ordinary
DOS prompt.

In the rest of this document, it is assumed that the reader is reasonably
familiar with MS-DOS commands, directories, and files. It is also assumed that
the reader is familiar with FITS files in general. No special knowledge of the
internal format of a FITS table is necessary to use FTB, but a user that is
unfamiliar with the concepts should read either the NOST document and/or Harten
et al. 1988. The NOST document is available in LaTEX, Postscript, and plain text
format by anonymous FTP from host NSSDCA.GSFC.NASA.GOV in the FITS subdirectory.


1.1   References

Brotzman, L.E., and Gessner, S.E. 1991, The Astronomical Data Center CD-ROM,
   Selected Astronomical Catalogs, Volume I, ADC Doc. No. STX-T-1-5002-009-91.

Harten, R.H., Grosbol, P., Greisen, E.W., and Wells, D.C. 1988, A&AS, 73, 365.

NASA Office of Standards and Technology (NOST) 1991, Draft FITS Implementation
   Standard, NOST Doc. No. 100-0.1g.


Page 2



 ____________________________________________________________________________
| Command |                            Description                           |
|_________|__________________________________________________________________|
| BROWSE  | Browse through table records on the computer screen              |
| CLOSE   | Close a table and free its allocated resources                   |
| DISPLAY | Define the fields to display with BROWSE and EXTRACT             |
| DOS     | Execute a DOS command or shell to a DOS prompt                   |
| ECHO    | Start or stop command line echo in FTB batch files               |
| EXECUTE | Execute an FTB batch file, i.e., a set of FTB commands in a text |
|         | file                                                             |
| EXIT    | Leave FTB                                                        |
| EXTRACT | Write selected records to a text file                            |
| HELP    | Get help on FTB commands                                         |
| LIST    | List the available tables, fields, header information, or FITS   |
|         | header to the screen, printer, or a text file                    |
| OPEN    | Open a FITS file, which may contain more than one table          |
| QUIT    | A synonym for EXIT                                               |
| REMARK  | Ignore the remainder of the input line; used in FTB batch files  |
| SELECT  | Define the records to display with BROWSE and EXTRACT by setting |
|         | selection criteria on certain fields                             |
| TABLE   | Set current table value                                          |
|_________|__________________________________________________________________|

                        Table 1: Summary of FTB Commands


Page 3

2    Installing FTB

The ADC FITS Table Browser requires an IBM PC/AT/XT or close compatible, any
kind of display (monochrome, CGA, EGA, or VGA), at least 256K of RAM, and MS-DOS
3.0 or higher. If you are using FTB to display FITS tables on the ADC CD-ROM,
the MS-DOS CD-ROM Extensions (MSCDEX) Version 2.0 or higher must be installed.

FTB is distributed on a single 360K 5.25" floppy diskette. The following files
appear in the root directory of the disk:

   FTB.EXE       Executable FITS Table Browser program.

   FTB.HLP       Input file for the HELP command.

   FTB.DOC       Printable ASCII version of this document.

   FTB.TEX       LaTEX source for this document.

   ADC.STY       LaTEX style file used by FTB.TEX.

   READ.ME       A text file containing any information that became available
                 after the User's Guide was printed.

   *.FTB         Example FTB batch files. These files are explained in more
                 detail later.

To install the program on a hard disk, create a new subdirectory and copy all
the files from the distribution disk into the subdirectory. For example:

   C:\> mkdir ftb
   C:\> chdir ftb
   C:\FTB> copy a:*.*
           .
           .
           .
   8 file(s) copied
   C:\FTB> ftb

FTB expects to find the help file, FTB.HLP, in the same subdirectory as FTB.EXE,
so it is very important that at least these two files are kept together.


Page 4

3    Starting up FTB

The FTB program is executed with the following optional command-line arguments:

     ftb [-f batch-file] [FITS-file]

Here "batch-file" is the name of a text file containing a set of FTB commands.
Batch files are useful for FITS tables that are accessed repeatedly. The batch
file can contain all the commands for opening the FITS file (OPEN command),
specifying the fields to display (DISPLAY command), and setting constraints on
field values to select which records to display (SELECT command). Batch files
are also used for pulling records out of the FITS tables and writing them to
plain text files (EXTRACT command).

"FITS-file" is the name of a FITS table to open automatically. It can either
be the fully-qualified pathname of the file, or a relative pathname from the
current working directory. For example:

   ftb l:\nonstell\nebulae\pln\pln.fit

will run FTB and open the Strasbourg Planetary Nebulae Catalog on the ADC CD-ROM
(assuming that the CD-ROM drive is assigned to drive letter L).

When FTB is started up, it first checks the command line for the "f" option (in
upper or lower case) and a batch file name. If found, the batch file is
executed. Then FTB looks at the command line for the name of a FITS table to
open. Finally, FTB goes into interactive mode, where it issues a prompt and
accepts commands from the user.


3.1   Entering FTB commands

In interactive mode, FTB issues a prompt that is very similar to the standard
DOS prompt. It starts with the label [FTB], followed by the current disk and
working directory:

   [FTB] C:\FTB>

FTB can recognize its commands regardless of whether they are in upper or lower
case and even when they are incomplete, for example, B, Br, bro, and bROWSe are
all equivalent to the command BROWSE. The only exceptions to this rule are the
EXIT and QUIT commands, which must be entered in full.

Commands may be continued onto additional input lines by putting a dash, "-", at
the end of each input line, however the total length of a command can not exceed
255 characters.

The most important command is HELP. When entered by itself, HELP prints the list
of commands given in Table 1. To get help with a specific command, enter HELP
<command>.


Page 5

4    Using FTB

FTB is not a complicated program. There are only a few commands and they were
constructed to be as simple as possible. The HELP command provides enough
information to use FTB, the only trick is to invoke the commands in the right
order.

The first thing to do is to OPEN a FITS file. Changing the current working
directory is accomplished by the DOS chdir (cd) command (remember that any
command the FTB can't recognize is passed on to DOS for execution). The OPEN
command expects the full name of the FITS file, including the extension.

After a file has been opened, the information from the FITS headers can be
written to the screen with the LIST command. Some examples of using LIST are
given in section 6.

Since a single FITS file can have many tables, and FTB can have more than one
FITS file open at a time, it's important to keep track of the tables. FTB
remembers the table that was accessed by each command in a value called the
"current table". All of the commands that manipulate data within a single table
(e.g. BROWSE or DISPLAY) have an optional parameter that allows the user to
override the value of the current table. Whenever the TABLE parameter is used,
the value of the current table is updated. If no table is specified, then FTB
assumes the command was meant for the current table. The TABLE command can be
used to inspect or change the setting of the current table value.

The BROWSE command prints the fields of the table to the computer screen. If
given no other information, FTB simply copies the fields from the table to the
screen in exactly the same format as they are stored. The DISPLAY command can be
used to select specific fields for display (or for writing out to a text file
with the EXTRACT command). With DISPLAY, it is possible to specify:

   1. a list of fields separated by blanks, e.g. RAH RAM RAS

   2. two fields concatenated together, e.g. DECSIGN+DECD

   3. a range of fields, e.g. RAH,DECS

   4. a field in a specific display column, e.g. NAME/72

It is also possible to limit the search to only those records that meet certain
criteria, such as magnitude or proper motion limits. The SELECT command has a
very simple grammer for entering logical expressions that define the acceptable
values for displaying records. Selections can be based on numerical ranges
(e.g. RADVEL lt 0.0) or substrings of character fields (e.g. NAME in 'BET LYR').


Page 6

5    Future Developments

This is the second release of FTB. Version 1.0 was released with the ADC CD-ROM
Test Disk in 1989. It was written in Pascal and had a signifigantly different
and more restrictive user interface.

Version 2.0.1 is written in C, and includes several new features, the most
significant of which is the ability to place search constraints on specific
fields. Still, there are several shortcomings of this version that are in the
process of being fixed.

Some of the deficiencies of FTB 2.0.1 are:

   1. FTB cannot write extracted data records in FITS format.

      This is the primary failing of FTB - that it writes out extracted data
      in a format that it can not read in again. A FITS-format extraction
      tool is currently in testing.


   2. Data stored on the ADC CD-ROM Text File Version, are not accessible.

      The Text File version of the ADC CD-ROM contains the same catalogs as the
      FITS File version, except each table is in a single flat text file, and
      the FITS header is in a separate text file. It should be possible to use
      FTB on either disk interchangably.


   3. Only sequential searches without data indexing are used.

      Searching for records in a table can be slow, especially on a CD-ROM.
      Applying fast indexing software to the FITS tables, so that searches are
      first run against the efficient indexes, rather than the inefficient
      CD-ROM would greatly improve access speeds.

All of these items are being worked on currently, with priority going to item
(1).


Page 7

6    FTB Command Reference

In the following, all FTB commands are given in alphabetical order. For each
command the command parameters and defaults are given, followed by a
description. Parameters enclosed in square brackets, "[]", are optional. When
there is a choice of parameters, the list is given with each parameter separated
by a vertical bar, "|". Elipses, "...", indicate that the previous parameter(s)
may be repeated.

A table-id can be either the name of a table, as given in the FITS header by the
EXTNAME keyword, or its sequential position in the list of active tables. For
example, given the following results from the LIST command:

   [FTB] L:\NONSTELL\GALAXIES\ESOUPP> open esoupp.fit

   [FTB] L:\NONSTELL\GALAXIES\ESOUPP> list

   There are 5 tables in 1 file

    1. ESOUpp_Data           ESO/Uppsala Survey of ESO(B) Atlas, Main Data
    2. ESOUpp_Notes          ESO/Uppsala Survey of ESO(B) Atlas, Notes
    3. ESOUpp_IDRefs         ESO/Uppsala Survey of ESO(B) Atlas, ID Refs.
    4. ESOUpp_MagRefs        ESO/Uppsala Survey, Mag. and Velocity Refs.
    5. ESOUpp_Plates         ESO/Uppsala Survey of ESO(B) Atlas, Plate Data

The table-id for the Notes table is either "ESOUpp_Notes" or "2".

Similarly, a field-id is the name of the field, as given by the TTYPE keyword in
the FITS header, or the field's sequential position in the header. Continuing
with the above example:

   [FTB] L:\NONSTELL\GALAXIES\ESOUPP> list table esoupp_notes fields

   Fld Col  Fmt      Name          Units        Description

      1   1  I2      RAH            h        Hours RA, equinox 1950
      2   3  I2      RAM            min      Minutes RA, equinox 1950
      3   5  I2      RAS            s        Seconds RA, equinox 1950
      4   7  A1      DecSign                 Sign Dec, equinox 1950
      5   8  I2      DecD           deg      Degrees Dec, equinox 1950
      6  10  F4.1    DecM           arcmin   Minutes Dec, equinox 1950
      7  15  A10     ESOUpp                  ESO/Uppsala identifier (see table
                                              ESOUpp_Data)
      8  26  A55     Note                    Text of note


The field-id for the ESO/Uppsala identifier is either "ESOUpp" or "7".


Page 8

6.1 BROWSE

Command: BROWSE [TABLE table-id] [RANGE start-finish]
Default: Current table; all records in the table

The BROWSE command allows one to browse through the given table. The table-id
can be either the table number or the table name. If no table identifier is
given, the current table (see TABLE) is browsed. The search begins at record
"start" and runs through record "finish" inclusive, the default is to start at
record 1 and proceed to the end of the table.


6.2   CLOSE

Command: CLOSE [TABLE table-id]
Default: Current table

The CLOSE command closes the given table and frees all allocated memory
attached to the table. Closing a table does not affect the ordering of the
table identifiers for other open tables. For example,

    CLOSE TABLE 2

will free all resources for table 2 and delete it from the list. Subsequent
LIST commands would show that item 2 is no longer on the list of tables, but
tables 1, 3, 4, ..., are left intact with the same numbers.


6.3   DISPLAY

Command: DISPLAY [TABLE table-id] [CLEAR] field-id ...
Default: None

The DISPLAY command allows the user to specify which fields are displayed by
BROWSE. The table-id can be either the table number or the table name. If no
table identifier is given, the field specifications apply to the current table.
The CLEAR option clears memory of all previous field specifications.

Field specifications may consist of the field number or name followed by a
separator character, and perhaps more information. A counter is maintained
which holds the next available screen column for a display. If a field will not
fit because some other field is in the way, it is moved to the right
automatically until a place is found for it, or until there is no more room.

Field separator characters can be one of the following:

   1. one or more blanks to indicate that a blank column should appear
      after the field

   2. a plus sign, "+", to indicate that the next field should be placed
      adjacent to this field

   3. a comma, ",", to indicate a range of fields to display, each separated
      by a single blank

   4. a slash, "/", followed by a column number to indicate that the field
      should be placed in that column.

Page 9

In cases (1), (2), and (3) the display counter is incremented to point to the
next available display position. In case (4), the display counter is not
changed.

For example, if the display counter starts at 1, the left margin, the following
field specifications:

    DISPLAY RAH RAM DECSIGN+DECD DECM MAG/30

will result in field RAH displayed starting in column 1 and field RAM
following, separated by a blank column. DECSIGN and DECD will be displayed
together without any intervening blank column. DECM will be separated from DECD
by a blank column, and MAG will be displayed starting in column 30. The display
counter is set to point to the column following DECM.

If those same six fields are adjacent to each other in the table (which can be
verified with the LIST FIELDS command), then the following field specification:

    DISPLAY RAH,MAG

will display all six fields, each separated by a single blank.


6.4   DOS

Command: DOS [DOS-command]
Default: Shell

The DOS command allows the user to execute any legal DOS command, program, or
batch file. The user should note that any command entered at the main FTB
prompt that is not recognized as a valid FTB command is automatically passed on
to DOS. The explicit DOS command is included to allow the user to execute a DOS
program whose name conflicts with a valid FTB command, for example LIST, and
also as a way to "shell" out to an active DOS command prompt. To reach a DOS
shell, simply enter "DOS" without any operands. To return to FTB, enter the DOS
command "EXIT".


6.5   ECHO

Command: ECHO [ON | OFF]
Default: Print current ECHO setting

The ECHO command starts or stops command-line echo in FTB batch files. It has
no effect on commands entered interactively. When set (ECHO ON), every command
line read from a batch file is echoed to the screen before it is executed.
Command-line echo is useful for tracing the execution of an FTB batch file.


Page 10

6.6   EXECUTE

Command: EXECUTE [filename]
Default: Prompt for filename

The EXECUTE command opens a text file containing a series of FTB commands and
executes them one at a time (batch processing). This is a convenient way of
opening a table file and setting up the display for tables that are used often.

All valid FTB commands are accepted, including those commands that are passed
on to DOS. Comments can appear in the batch file using the REMARK command. Long
commands can be spread out over several lines by placing the continuation
character, "-", at the end of each line to be continued. No command line can
total more than 255 characters in length.


6.7   EXIT

Command: EXIT
Default: None

The EXIT command terminates FTB, closing all open files and restoring the
original default drive and directory.


6.8   EXTRACT

Command: EXTRACT [TABLE table-id] [RANGE start-finish] [filename]
Default: Current table; all records; prompt for filename

The EXTRACT command stores selected records (see SELECT) into the named text
file in the same format as would be displayed on the screen (see DISPLAY). The
search begins at record "start" and runs through record "finish" inclusive,
the default is to start at record 1 and proceed to the end of the table.

Example:

   extract table 2 range 200-550 savedata.txt

This will extract the records in table 2 into file SAVEDATA.TXT. The search
begins at record 200 and proceeds through record 550. The number of records
extracted depends on the criteria set by the SELECT command.


6.9   HELP

Command: HELP [command]
Default: Command list

The HELP command presents informative text about the FTB commands.


Page 11

6.10   LIST

Command: LIST [TABLE table-id] [ FIELDS | HEADER | INFO ]
         [SCREEN | PRINTER | FILE [filename]]
Default: List of tables; output to screen

By default, the LIST command lists the active tables by number and by name (if
available). It will also print a listing of the field information, the actual
FITS header for a specific table, or a more human-readable version of the table
header information.

Output can be directed to the screen, the printer, or a disk file. To send
output to a file, the FILE option should always appear last on the command
line. If no file name is given, the user is prompted for one.

Example:

   list table 2 header file tabinfo.hdr

This will generate a listing of the FITS header for table 2 in the text file
TABINFO.HDR in the current working directory.


6.11   OPEN

Command: OPEN [filename]
Default: Prompt for filename

The OPEN command opens a FITS file, scans the file for standard ASCII tables
(XTENSION= 'TABLE '), and decodes the table headers to determine the
information needed to browse through the table.

The file must be accessible through the current working directory (given in the
main FTB command prompt), or by explicitly giving the absolute or relative
pathname.


6.12   QUIT

Command: QUIT
Default: None

The QUIT command is a synonym for EXIT, which terminates FTB, closing all open
files and restoring the original default drive and directory.


6.13   REMARK

Command: REMARK [comments in any format]
Default: None

The REMARK command is used to include comments in FTB batch files (see
EXECUTE). REMARK can be entered at the FTB command prompt, although it isn't
very useful to do so.


Page 12

6.14   SELECT

Command: SELECT [TABLE table-id] [ [CLEAR] | [ [CURRENT AND_OR] conditions ] ]
Default: List of current selections

The SELECT command specifies which records are displayed by placing constraints
on field values. Only those records meeting the criteria set down by the
conditions will be displayed by the BROWSE command or written to disk by the
EXTRACT command. The CLEAR option clears out all previously defined
conditions. The CURRENT option is used to add the specified conditions to any
that were defined previously.

The conditions are a series of relational expressions in the form:

   field-id relational-operator limiting-value

Relational operators are as follows:

    EQ equal to                    NE not equal to
    LT less than                   GT greater than
    LE less than or equal to       GE greater than or equal to
    SE strictly equal to           IN contains substring

The limiting value must be of the same type as the specified field, e.g., if
the field is an integer, the limiting value must be given as an integer.
Strings must be delimited by a character that is not contained within the
subject strings themselves, as in: 'string' or "quoted 'string'".

For strings, the operators EQ, NE, LT, GT, LE, and GE, ignore case and trailing
blanks. The operators SE and IN are only used for string comparisons. For
SE, strictly equal to, case and trailing blanks are significant, therefore the
comparison value must have the same length as the field value. IN, for testing
substrings, is case insensitive.

Up to ten (10) conditions can be specified, and each must be related through
the relational operators AND or OR. All conditions are evaluated from left to
right. If the expression is evaluated as FALSE, the record has failed the test
and will not be selected for display or extraction. If the expression is
evaluated as TRUE, then the record is selected. No grouping with parentheses is
allowed.

For example, to display only the records for objects in Table 1 appearing west
of 3 hours of right ascension, up to and including 6 hours of RA, and north of
15 degrees declination, enter:

   SELECT Table 1 RAH gt 3 and RAH le 6 and DecSign eq '+' and DecD lt 15

To add a condition to display all stars with visual magnitude brighter than 6,
regardless of position in the sky, enter:

   SELECT CURRENT or V lt 6

To eliminate the selection criteria and display all records, enter:

   SELECT CLEAR


Page 13

6.15   TABLE

Command: TABLE [table-id]
Default: List current table-id

The TABLE command sets the value of the current table identifier. If no new
value is given, the number and name of the current table is displayed on the
screen.


7    Receiving Updates

FTB is available by anonymous FTP from Internet node NDADSA.GSFC.NASA.GOV (IP
address 128.183.36.17) in the ADC directory under SOFTWARE. The same files are
available by DECNET copy in directory NDADSA::ANON_DIR:[ADC.SOFTWARE].
Distributions on floppy diskette are available from the NSSDC Coordinated
Request and User Support Office (CRUSO) at:

    Coordinated Request and User Support Office
    National Space Science Data Center
    Mail Code 933.4
    NASA Goddard Space Flight Center
    Greenbelt, MD 20771
    (voice)  (301) 286-6695
    (FAX)  (301) 286-4952
    (Email) REQUEST@NSSDCA.GSFC.NASA.GOV


8    Acknowledgments

Archie Warnock and Daniel Klinglesmith were very helpful during the beta
testing of Version 2.0.0. I would also like to thank Jaylee Mead and Michael
Van Steenberg, for without them, the ADC CD ROM, ADC FITS Table Browser, and
indeed the ADC itself wouldn't exist.