PDS_VERSION_ID            = PDS3

LABEL_REVISION_NOTE       = "T. Farnham 2006-07-07"

RECORD_TYPE               = STREAM

OBJECT                    = INSTRUMENT

INSTRUMENT_HOST_ID      = "SDU"

INSTRUMENT_ID           = "SRC"

OBJECT                  = INSTRUMENT_INFORMATION

INSTRUMENT_NAME       = "SAMPLE RETURN CAPSULE"

INSTRUMENT_TYPE       = "DUST SAMPLE COLLECTOR"

INSTRUMENT_DESC       = "

The descriptions in this file were written by Tony Farnham using

information from the ``Stardust Mission Plan document'' (used by

permission from the Stardust project).

Instrument description

-----------------------

The Sample Return Capsule (SRC) was a system for non-destructively

collecting cometary and interstellar dust particles, then storing the

samples and returning them to the Earth for detailed analysis.

The Sample Return Capsule was about a meter in diameter, and opened

like a clamshell, allowing the collecting grid to be deployed into the

dust stream to collect samples.  The SRC was mounted along the negative x-axis

of the Stardust spacecraft.  It consisted of four main components: the

sample collector, the aeroshell (backshell and heat shield), the

parachute system, and the avionics.

Sample Collector

----------------

The sample collector was a passive system for collecting dust

grains.  It consisted of an aluminum grid encasing multiple

microporous silica aerogel blocks that acted as the dust

collectors.  The grid array was exposed to a stream of dust

particles, which were gradually slowed by the low-density aerogel.

The aerogel dissipated the kinetic energy of the particles so they

were not destroyed during the collection process.  Graded density

media were used to give even lower density for the initial impact.

The aerogel collector grid allowed collection from both sides.  One

side of the collector (facing the +x direction) was used to collect

samples during the comet encounter and the opposite side was used

for interstellar dust collection.  Each side of the collector

contained a total of 1000 cm^2 of useful collecting area.

After the samples were obtained, the collector grid could fold up

into a compact configuration in the sample return capsule.  Stowage

of the collector was achieved by first folding the collector grid

onto the boom via the wrist joint and then folding the boom/collector

into the SRC canister via the shoulder joint.

In addition to allowing the collector grid to fold up into the SRC,

where it was protected, this deployment mechanism was the key for

maximizing the amount of time available for the capture of

interstellar dust particles. The mechanism allowed the collector to

be steered via the wrist joint about the spacecraft y-axis toward

the negative z-axis. The collector field-of-view remained unobstructed by

the SRC backshield for 51 degrees of this motion, half the grid was

in shadow at 63 degrees, and all of the grid was in shadow at 75

degrees.  (Note that for the shadow definition, the interstellar particle (ISP) stream is

assumed to be incoming perpendicular to the aerogel grid.) It is

worth noting that the collector field-of-view would remain

completely unobstructed for 65 degrees of the motion should the

shoulder joint be used during interstellar dust particle

collection.  However, usage of the shoulder joint with the

collector fully deployed was considered to be an unnecessary risk.

Aeroshell

---------

The aeroshell was used to protect the SRC during the cruise phases

and during re-entry into the Earth's atmosphere.  During re-entry,

the aeroshell dissipated over 99 percent of the initial kinetic energy

of the vehicle and protected the sample canister against the extreme

aerodynamic heating of atmospheric entry.  The heat shield was a 60

degree half angle blunt cone made of a graphite/epoxy composite

covered with a thermal protection system.  Ablative material was

also applied to the backshell to protect the capsule from the

effects of recirculation flow.

Parachute System

----------------

During the entry and descent phases, a G-switch initiated timer with

What is a G-switch?  A "gravity" switch?

backup pressure sensors provided the required parachute deployment

timing.  The parachute system incorporated a drogue and main chute

into a single parachute canister.  The parachute canister contained a

mortar tube that held the drogue chute. A gas cartridge was housed

outside the canister and was used to pressurize the mortar tube and

expel the drogue chute.  The drogue chute was used to stabilize the

descending SRC through the transonic and subsonic atmospheric

regimes. The drogue was discarded using one of two redundant cutters,

extracting the main chute as it moves away from the SRC. Upon ground

impact, a cutter in the riser of the main chute was commanded by a

G-switch, separating the main chute from the SRC to prevent surface

winds from dragging the SRC across the ground.

Avionics

--------

The avionics design included a UHF locator beacon used as an SRC

location aid for the ground recovery team.  The beacon was activated

upon main chute deployment.  It was powered by a set of primary cell

lithium sulfur dioxide batteries, which had enough capacity to

operate the beacon for 40 hours. Additional SRC tracking was provided

by skin tracking from two C-band radar sites at the Utah Test and

Training Range (UTTR) landing site. A mylar target mounted on the main

chute provides an equivalent one square meter of radar cross section.

Earth Return Sequence

---------------------

On January 15, 2006, the Sample Return Capsule returned to the Earth.

Prior to separation, the spacecraft was placed at the separation

attitude and the SRC was spun up using a spin release mechanism. This

provided the spin stabilization that the SRC required for successful

atmospheric entry.  After the SRC separated, the spacecraft executed a

divert maneuver, to put it into a heliocentric orbit.

The SRC entered the atmosphere at 09:57 UTC on January 15, 2006.  The

SRC continued to free-fall to an altitude of about 3 km, at which

point the parachute deployed, allowing the SRC to land safely at the

Utah Test and Training Range.  It was recovered and transported to a

staging area at UTTR for retrieval of the sample canister, which was

then be transported to the planetary materials curatorial facility at

Johnson Space Center.

"

END_OBJECT              = INSTRUMENT_INFORMATION

OBJECT                  = INSTRUMENT_REFERENCE_INFO

REFERENCE_KEY_ID      = "N/A"

END_OBJECT              = INSTRUMENT_REFERENCE_INFO

END_OBJECT                = INSTRUMENT

END