PDS_VERSION_ID  = PDS3

LABEL_REVISION_NOTE     = "H. TAYLOR, 2000-09-14;

B. SEMENOV, 2003-02-25;

B. SEMENOV, 2004-06-10

T. FARNHAM, 2006-07-10"

RECORD_TYPE     = STREAM

OBJECT  = MISSION

MISSION_NAME  = "STARDUST"

OBJECT        = MISSION_INFORMATION

MISSION_START_DATE  = 1999-02-07

MISSION_STOP_DATE   = UNK

MISSION_ALIAS_NAME  = "N/A"

MISSION_DESC        = "

The descriptions given here were originally copied from the

``Stardust Mission Plan'' document and its addenda (used with

permission from the Stardust project).  To reflect the

completion of the primary mission, the information has been

updated by Tony Farnham using the weekly status reports, press

releases and informational bulletins distributed by the Stardust

mission.

Mission Overview

================

The primary science goal of the STARDUST mission was to collect

Wild 2 coma samples, plus bonus interstellar dust samples, in

aerogel, and return them to Earth.  On January 2, 2004, the

spacecraft successfully flew by the comet, obtaining dust

samples that were returned to the Earth on January 15, 2006.

Additional science return was obtained in the form of images of

the comet coma and nucleus obtained with the NAVCAM, in situ dust

composition measurements obtained with the Comet and

Interstellar Dust Analyzer (CIDA) and dust impact counts from

the Dust Flux Monitor (DFMI).

Trajectory

----------

The STARDUST mission was designed for a low velocity (6.1

km/s) flyby of comet Wild 2 during a time when the comet was

moderately active (at a solar distance of 1.9 AU).  The

spacecraft was then designed to have a low energy Earth

returning trajectory so that dust samples obtained at the

comet could safely be returned to Earth.

The launch on February 7 1999 put Stardust into a two year

orbit, which would bring it back to Earth for a gravitational

assist in 2001.  Deep Space Maneuver #1 (DSM1), broken into

three separate burns, was executed on January 18, 20 and 22,

2000, when Stardust was near aphelion.  This maneuver imparted

a 170 m/s deterministic delta-V to set up the orbit for an

Earth flyby, which occurred on January 15, 2001.  The Earth

flyby increased the period of the spacecraft's orbit so that

Stardust could reach comet Wild 2.  The new orbit had a 2.5

year period.  A small, 2.65 m/s, deep space maneuver (DSM2)

was executed on January 24, 2002 to correct for minor

trajectory errors from the previous Earth flyby.  On June

17-18, 2003, the third deep space maneuver (DSM3) was

performed to target Wild 2 properly.  It imparted a Delta-V

of 69 m/s.  On January 2, 2004, Stardust encountered Comet

Wild 2 (98.5 days after the comet's perihelion passage),

passing at a distance of 237 km.  The last deep space

maneuver, DSM4, was performed in the first week of February

2004.  It was a small maneuver (5 m/s) and adjusted the orbit

to target the spacecraft back to Earth so the Sample Return

Capsule could reenter the atmosphere and parachute to the

recovery site in Utah.

Asteroid 5535 Annefrank Encounter

----------------------------------

On November 2, 2002 04:50:20 UTC, Stardust encountered the

asteroid 5535 Annefrank.  The encounter distance was 3079 km

and the solar phase angle ranged from 130 deg to 47 degrees

during the period of observations.  This encounter was used as

an engineering test of the spacecraft and ground operations in

preparation for the encounter with comet Wild 2.

Comet Encounter

---------------

On January 2, 2004, 19:21:28 UTC, Stardust encountered Comet

Wild 2 (98.5 days after the comet's perihelion passage).  The

spacecraft passed the comet on the sunward side with a

relative velocity of 6.1 km/sec.  The closest approach

distance was 237 km (+/- 1km).  (The original encounter

distance was planned to be 150 km, but this was changed after

a safety review board decided to increase the closest approach

distance to minimize the potential for catastrophic dust

collisions.)

The relative velocity between the comet and the spacecraft was

such that the comet actually overtook the spacecraft from

behind as they traveled around the Sun.  During the encounter,

the spacecraft was on the sun-lit side of the nucleus,

approaching at a solar phase angle of 70 degrees, reaching a

minimum angle of 3 degrees near closest approach and departing

at a phase angle of 110 degrees.

Interstellar Dust Collection

----------------------------

The interstellar dust particle (ISP) collection periods

occurred near the first and second aphelion portions of the

spacecraft's orbit, when the relative velocity between the

spacecraft and the ISP streams is at a minimum.  In addition

to the favorable velocity alignment, these collection periods

are further defined by the need to avoid large off-Sun

pointing of the solar panels, collection of beta meteoroids,

and deep space maneuvers.

The first ISP collection period lasted from February 22

through May 1, 2000.  The second collection period was from

August 5 through December 9, 2002.  Although the opportunity

existed for additional ISP collection on the third orbit, this

would have been after the Wild 2 encounter, and it was decided

that it was undesirable to re-open the SRC after comet

encounter.

In Situ Particle Analysis

-------------------------

CIDA and DFMI experiments were executed at every available

opportunity during the mission. The main constraints on their

operation were the availability of spacecraft power and

conflicts with other mission activities. Prime experiment

periods were defined as those where the interstellar particle

(ISP) streams are oriented to fall within the CIDA

field-of-view.

Earth Return

------------

On January 15, 2006 the Sample Return Capsule (SRC)

successfully separated from the Stardust spacecraft.  After

separation, the spacecraft executed a divert maneuver that put

it into a heliocentric orbit, while the SRC re-entered the

Earth's atmosphere and parachuted to the ground.  The SRC was

recovered at the Utah Test and Training Range (UTTR) and

transported to the staging area at UTTR for the retrieval of

the sample canister.  The canister was then transported to the

planetary materials curatorial facility at Johnson Space

Center in Houston.

Mission Phases

==============

Six mission phases were originally defined for significant

spacecraft activity periods. These were the Launch, Cruise 1,

Earth Gravity Assist, Cruise 2, Wild 2 Encounter, Cruise 3,

and Earth Return. One more mission phase -- Annefrank

Encounter, -- completely nested inside the Cruise 2 was

added in 2002 when the asteroid flyby was approved

as a full scale Wild 2 encounter test.

LAUNCH

------

Mission Phase Start Time       : 1999-02-07

Mission Phase Stop Time        : 1999-03-08

The launch phase began as the launch vehicle lifted-off and

ended with the completion of the activation and checkout of

most of the spacecraft subsystems. Included in this phase

were spacecraft separation from the launch vehicle,

establishment of attitude and communications, tracking of the

spacecraft and the execution of the first trajectory

correction maneuver (TCM-1) to correct the injection error.

The duration of this phase was 30 days.

CRUISE 1

--------

Mission Phase Start Time       : 1999-03-08

Mission Phase Stop Time        : 2000-11-14

The Cruise 1 phase of the first part of the STARDUST mission,

nearly six years long, was a period of relatively low

activity.  This part spanned from launch through the Earth

flyby. Within this phase are embedded the first ISP collection

period and the CIDA and DFMI experiments. The ISP collection

period during this phase of the mission started 380 days after

launch and continued for 69 days.

EARTH GRAVITY ASSIST

--------------------

Mission Phase Start Time       : 2000-11-14

Mission Phase Stop Time        : 2001-02-14

The Earth flyby was performed primarily to provide a gravity

assist to the STARDUST spacecraft thus reducing the delta-V

requirements of the mission. The flyby changed the orbital

period from 2 years to about 2.5 years. The spacecraft

approached Earth from the dark side with a velocity of 6.5

km/s and receded back into the dark side having flown by the

sunward side at a closest approach altitude of

6008 km. During the flyby the Sun-Earth-spacecraft angle cycled

from ~130 degrees to ~28 degrees at closest approach to a

minimum of ~19 degrees (8 minutes after closest approach) and

back up to ~90 degrees toward the end of the EGA phase. The

Earth flyby time was 15 January 2001 11:14:28 UTC.

CRUISE 2

--------

Mission Phase Start Time       : 2001-02-14

Mission Phase Stop Time        : 2003-09-24

The Cruise 2 phase was the second part of cruise, spanning the

time between the Earth flyby and the Wild 2 encounter. Within

this phase are embedded the second ISP collection period and

the CIDA and DFMI experiments. The ISP collection period

during this phase of the mission started 1275 days after

launch and continued for 126 days.

ANNEFRANK ENCOUNTER

-------------------

Mission Phase Start Time       : 2002-10-31

Mission Phase Stop Time        : 2002-11-05

This phase was the part of the mission, during which STARDUST

flew by the S-type, main belt asteroid Annefrank. The

Annefrank flyby occurred with just over one month (out of four)

remaining in the second ISP collection period and was fully

embedded within the Cruise 2 phase of the mission.

This encounter was not present in original mission plan and

was added in 2002 as a full scale Wild 2 encounter test.

The main objective and supporting rationale for this test was

to implement the entire Wild 2 encounter sequence in flight

at Annefrank.

The spacecraft flew past Annefrank on 2 November 2002 at

4:51:20 UTC and a closest approach distance of 3079 km.  The

imaging sequence encompassed a solar phase angle range from

130 deg to 47 deg.

WILD 2 ENCOUNTER

----------------

Mission Phase Start Time       : 2003-09-24

Mission Phase Stop Time        : 2004-02-21

The most important mission phase of STARDUST ranged from 100

days before the encounter with comet Wild 2 to 50 days after.

Encounter occurred on January 2, 2004, 19:21:28 UTC.

The primary goal of obtaining comet coma samples during the

encounter flyby was accomplished by a navigation plan that

delivered the spacecraft to a close approach distance of 237

km from the nucleus.  Near the closest encounter, the

spacecraft positive x-axis was aligned with the S/C velocity vector

relative to Wild 2 so that the dust shield protected the

S/C. In this flyby configuration, the Earth was located in the

direction of the spacecraft positive z-axis (also HGA direction). The

spacecraft approached Wild 2 from above and receded under the

comet's orbit plane.

Although the collection of cometary dust samples was the

primary goal of the mission, it was totally passive, enabled by

deployment of the aerogel collector and the setting of the

spacecraft / collector attitude perpendicular to the dust

stream.  The collector was deployed on December 24, 2003 and

remained deployed until five hours after the encounter, at

which time the spacecraft should have exited the coma.  The

majority of the dust was believed to have been collected in the few

hours around closest approach.

CRUISE 3

--------

Mission Phase Start Time       : 2004-02-21

Mission Phase Stop Time        : 2005-10-17

The Cruise 3 phase was the third part of cruise, spanning from

the Wild 2 encounter to the return to Earth. During this

period, no dust collection took place.  The dust collectors

were stowed to protect the comet particles and to prevent any

potential problems that might endanger their return to the

Earth.

EARTH RETURN

------------

Mission Phase Start Time       : 2005-10-17

Mission Phase Stop Time        : 2006-01-16

This phase of the mission began 90 days before Earth Return

(ER) and ended when the SRC was transferred to the ground

handling team. Earth approach contained three TCM's and a

final divert maneuver, performed after SRC separation, to

prevent the spacecraft from following the SRC into the Earth's

atmosphere. Prior to separation, the spacecraft was placed at

the separation attitude and the SRC was spun up using a spin

release mechanism. This provided the spin stabilization that

the SRC required for successful atmospheric entry.  The SRC

entered the atmosphere at 09:57 UTC on January 15, 2006.

The SRC aeroshell protected the sample canister against

the extreme aerodynamic heating experienced during

atmospheric entry. The aeroshell also dissipated over 99 percent

of the initial kinetic energy thus allowing the parachute

system to place the SRC within the allowable touchdown

requirements."

MISSION_OBJECTIVES_SUMMARY = "

The primary science goal of the STARDUST mission was to collect

Wild 2 coma samples, plus bonus interstellar dust samples, in

aerogel, and return them to Earth. Additional science return

included images of the comet coma and nucleus, and in situ

measurements of the compositions of dust grains from the Comet

and Interstellar Dust Analyzer (CIDA) and particle impact counts

from the Dust Flux Monitor (DFM) mounted on the comet dust

shield.

These science goals lead to the following objectives in the

design of the STARDUST mission:

1) Provide a flyby of a comet of interest (Wild 2) at a

sufficiently low velocity (less than 6.5 km/s) such that

non-destructive capture of comet dust is possible using an

aerogel collector.

2) Facilitate the intercept of significant numbers of

interstellar dust particles using the same collection medium,

also at as low a velocity as possible.

3) Return as many high resolution images of the comet coma and

nucleus as possible, subject to the cost constraints of the

mission."

END_OBJECT    = MISSION_INFORMATION

OBJECT        = MISSION_HOST

INSTRUMENT_HOST_ID  = "SDU"

OBJECT      = MISSION_TARGET

TARGET_NAME       = "81P/WILD 2 (1978 A2)"

END_OBJECT  = MISSION_TARGET

OBJECT      = MISSION_TARGET

TARGET_NAME       = "5535 ANNEFRANK"

END_OBJECT  = MISSION_TARGET

END_OBJECT    = MISSION_HOST

OBJECT        = MISSION_REFERENCE_INFORMATION

REFERENCE_KEY_ID    = "BROWNLEEETAL2003"

END_OBJECT    = MISSION_REFERENCE_INFORMATION

OBJECT        = MISSION_REFERENCE_INFORMATION

REFERENCE_KEY_ID    = "TSOUETAL2003"

END_OBJECT    = MISSION_REFERENCE_INFORMATION

END_OBJECT      = MISSION

END