***** File MODE_FIT.DOC                                                       
                                                                              
Mission: VEGA 1                                                               
Instrument: PUMA                                                              
Submission: IKI FITS Files                                                    
                                                                              
                                                                              
Original Format                                                               
                                                                              
    The data for these files were received as 4027 separate FITS files, each  
    containing a single PUMA spectrum in a binary form.  Each file began with 
    the same sequence of parameter values.  The spectrum followed these in a  
    format which varied slightly with spectrum mode.  In the amplitude sample 
    bytes of the spectra, the sign bit was as a flag bit to indicate amplitude
                                                                              
    triggered samples.  In this form a value of 1 (sign bit set) indicated a  
    non-triggered value.                                                      
                                                                              
                                                                              
Reformatting at SBN                                                           
                                                                              
    A program was written to take each FITS file, re-order the parameter      
    values slightly, and modify the treatment of flagged samples in the       
    spectra.  The resulting binary files were sorted and combined into        
    tables for each mode.                                                     
                                                                              
    Specifically:                                                             
                                                                              
      o  The sign bit in all spectrum samples was turned off.                 
                                                                              
      o  The mode 1, 2 and 3 spectra, the only ones which included sample     
         flagging, were expanded so that a separate flag field could be       
         associated with each amplitude sample.                               
                                                                              
      o  Where the sample had previously been flagged as amplitude-triggered  
         (original sign bit not equal to 1), the accompanying flag byte was   
         set equal to 1.                                                      
                                                                              
      o  The spectrum length parameter was adjusted to give the total number  
         of bytes in the spectrum itself, without the parameter values. (The  
         length of the parameter values was included in the original field.)  
                                                                              
      o  All spectra were then padded with nulls (zeroes) out to the maximum  
         spectrum length of the particular mode.                              
                                                                              
      o  The converted spectra were then collected into a single fixed-length 
         table for each mode.  The original ordering of the spectra (by FITS  
         file number) was maintained within each table, as this was assumed to
         be chronological.                                                    
                                                                              
                                                                              
Known Anomalies/Problems:                                                     
                                                                              
      o  Little or no explanation was available for some of the parameters in 
         the spectrum headers.  This is indicated in the DESCRIPTION part of  
         the PDS label for these datasets.                                    
                                                                              
      o  There are fewer spectra in this submission than in the binary table  
         also submitted by IKI or the text files submitted by MPI.  These data
         appear to be a strict subset of the IKI binary table, with most but  
         not all of the "extra" spectra in the second IKI submission having   
         later time values than the spectra in this dataset.  However, while  
         there is a large amount of overlap between the IKI and MPI           
         submission, each contains spectra not included in the other.         
                                                                              
      o  It has not yet been possible to translate the times in this file,    
         which are apparently in units of seconds, to UT.